## Slide 1: Federal Communications Commission Overview
William Hurst
Chief, Technical Research Branch
Federal Communications Commission
Office of Engineering and Technology
Laboratory Division

## Slide 2: Overview
Knowledge Database
Measurement Techniques
Recent FCC Actions
Mutual Recognition Agreement Status

## Slide 3: Knowledge Database (KDB)
The KDB Website is: www.fcc.gov/labhelp
  Web based database
    Detail Criteria Search
      Frequently Asked Questions (FAQ)
      Interpretations
      Measurement techniques
    Submission of inquiries
    Full text search
LABHELP@FCC.GOV email system is being phased out

## Slide 4: Measurement Techniques
Section 2.947 - Measurement Procedures
The Commission will accept data which has been measured in accordance with:
  Those set forth in bulletins or reports prepared by the Commission's Office of Engineering and Technology.
  Those acceptable to the Commission and published by national engineering societies such as the EIA, the IEEE, and ANSI.
  Any measurement procedure acceptable to the Commission may be used to prepare data demonstrating compliance with the FCC requirements.

## Slide 5: Measurement Techniques
The test report should include:
  Completely identify the specific standard or measurement procedures actually used
  A listing of the test equipment used
  Detailed description of measurement procedures actually used when they differ from published procedures
  As necessary the FCC may require additional information concerning measurement procedure used
Notes: Measurement Standards - 15.31(b)
  Strongly encouraged to use specific measurement procedures listed in Part 15.
  When using other procedures you should contact the FCC staff to ensure that such procedures can be relied on to produce measurement results compatible with the FCC measurement procedures.
  The description of the measurement procedure used in testing the equipment for compliance and a list of the test equipment actually employed shall be made part of an application/test report.

## Slide 6: What Measurement Techniques Should Be Used?
A number of measurement techniques have been identified and can be found in:
  FCC Rules
  Industry Standards
  Text of the Report and Order
  Public Notice Issued by the Commission
  Knowledge Database
List of FCC Related measurement techniques
  http://www.fcc.gov/oet/ea/Welcome.html

## Slide 7: Recent FCC Actions
FCC Approves First Software Defined Radio
  Software defined radios can change the frequency range, modulation type and/or output power of a radio device without making changes to hardware components.
  See FCC News Release: DOC-254463
Music Devices that connect to a personal computer
  See Public Notice DA 04-2253
Notes: FCC Approves First Software Defined Radio
The FCC has approved, for the first time, use of a software defined radio. This new type of equipment allows users to share limited radio spectrum, increases flexibility and reduces interference concerns. The Laboratory Division of the Commission’s Office of Engineering and Technology issued a Grant of Certification to Vanu, Inc., a software development company, for a cellular base station transmitter.
Software defined radios can change the frequency range, modulation type and/or output power of a radio device without making changes to hardware components. This programmability permits radios to be highly adaptable to changing needs, protocols and environments. (See FCC News Release: DOC-254463)
Approving Music Devices that Connect to a Personal Computer
The FCC issued a Public Notice to clarify the equipment authorization requirements for electronic musical instruments, recorders, amplifiers, and other sound creation and enhancement devices that are intended for or are capable of use with a personal computer.
Recently, many types of musical equipment have been introduced that are designed to connect directly to personal computers via standardized personal computer interfaces such as a USB or IEEE 1394 port. Such devices are then considered computer peripherals, which have a separate equipment approval process. Such devices, when marketed for use in residential areas (Class B devices), are required to follow the Declaration of Conformity (DoC) or certification process. DoC is a self-approval process similar to Verification except that it requires that the tests be performed by an accredited test laboratory. (See Public Notice: DA 04-2253)

## Slide 8: Recent FCC Actions
Modification of Parts 2 and 15
  Mandatory Electronic filing of applications or Grantee code.
  Reassess test labs every two years by Accrediting Body.
  Re-accredit and Reassess TCBs every two years.
  See FCC Report and Orders: FCC 04-165
Notes: Modification of Parts 2 and 15 of the FCC’s Rules
The FCC adopted changes to several technical rules for unlicensed radiofrequency devices contained in Parts 2 and 15 of its rules. As part of this Order the FCC updated the measurement procedure reference in section 15.35 to C63.4-2003.
With regards to laboratory accreditation the Order modified Section 2.948 to clarify that all test sites must be reassessed by their Accrediting Body every two years. Additionally, the Order modified Section 2.962 to clarify that every Telecommunications Certification Body (TCB) must be reassessed on two-year intervals. (See FCC Report and Orders: FCC 04-165)

## Slide 9: Recent FCC Actions
Updated Reference to C63.4-2003
ANSI C63.4 is incorporated into the FCC Rules by reference in three rule sections:
  2.948(b)(8)(i) – Description of measurement facilities
  15.31(a)(3) – Measurement Standards
  15.38(b)(6) – Incorporation by reference
The latest edition of ANSI C63.4-2003 was incorporated into the rules in FCC ET Docket 03-201, FCC 04-165, adopted on 7/8/04 (http://hraunfoss.fcc.gov/edocs_public/attachmatch/FCC-04-165A1.doc)
ANSI C63.4 may be used for most devices subjects to Part 15 of the FCC Rules, but not all

## Slide 10: Recent FCC Actions
Smart Antenna Systems
  Applies ONLY to Section 15.247 devices in the 2.4 GHz band. i.e. Does not apply to 5 GHz devices!
  Must comply with all requirements in Section 15.247(c)2i-iv.
    Must form multiple beams.
    Different information to each receiver
    Aggregate power to antenna/array for a Single Beam must not exceed appropriate limit for single P2P system based on array gain.
    Aggregate power to antenna/array for simultaneous beams must not exceed single beam limit by 8 dB
    Overlapping beams cannot exceed appropriate limit for a single beam.
Notes: Smart Antenna Systems
Beams
  Beamwidth not specified.
  Multiple beams must be formed sequentially or simultaneously.
  Each beam cannot exceed limits for single P2Psystem based on array gain.
  Each beam must send different information to different receivers.
    Broadcasting not allowed. i.e.Communicating the same information intended for multiple receivers at the same time. Broadcast of incidental control messages (i.e., ARP) to multiple receivers simultaneously is permitted. Independent Internet traffic to multiple receivers is not considered as broadcasting.
  Aggregate power on all beams < 8 dB above limit.
    6 beams at full power can be formed
  Overlapping beams cannot exceed single beam limit.

## Slide 11: Advanced Wireless Transmitters
Spread Spectrum Rules Adopted
UNII Rules Adopted
Digital Modulation Techniques allowed

## Slide 12: Recent FCC Actions
Broadband over Powerline (BPL)
  New option for broadband to the home (“last mile”)
  Recent rule changes to facilitate deployment
  Protect incumbent spectrum users from spurious emissions
  Recently established test procedures including technical standards for operation
  See FCC Report and Order: FCC 04-245
Notes: FCC Adopts Rules for Broadband over Powerline
The FCC has adopted changes to Part 15 of its rules to encourage the development of Access Broadband over Power Line (Access BPL) systems while safeguarding existing licensed services against harmful interference. Access BPL is a new technology that provides access to high speed broadband services using the largely untapped communications capabilities of the nation’s power grid.
In the Order adopting these changes, the Commission recognized the significant concerns of some licensed radio service users regarding the potential of Access BPL systems to cause interference to their operations. The Commission stated that its intention in adopting the Part 15 rule changes was to ensure that Access BPL operations do not become a source of harmful interference to licensed radio services. The rule changes in the Order establish specific technical and administrative requirements for Access BPL equipment and operators. The Order also sets forth procedures to measure the radio frequency (RF) energy emitted by Access BPL equipment. (See FCC Report and Order: FCC 04-245)

## Slide 13: MRA Implementation
APEC Tel MRA
  Canada
    Phase I – 33 US and 9 Canadian Accredited Labs
    Phase II – 11 US and 1 Canadian Certification Bodies
  Singapore
    Phase I – 25 US and 2 Singapore Accredited Labs
    Phase II – In process of accrediting Certification Bodies
  Taiwan (Phase 1 operational)
  Australia (Phase 1 operational)
  Japan (Phase 1 and 2 pending)
  Korea (Phase 1 signed)
  Hong Kong (Phase 1 and 2 signed)

## Slide 14
William S. Hurst Federal Communications Commission Office of Engineering and Technology William.Hurst@fcc.gov