## Slide 1: ANSI C63 COMMITTEE SC/2 TERMINOLOGY Status of ANSI C63.14 Update
Dave Southworth, SC/2 Chair
SPAWARSYSCEN - San Diego

## Slide 2: PINS FOR UPDATE
PINS Drafted
  Emailed: April 29, 2004 to C63 Secretary and others
  Established Update Requirement for C63.14
    American National Standard Dictionary for Technologies of Electromagnetic Compatibility (EMC), Electromagnetic Pulse (EMP), and Electrostatic Discharge (ESD)

## Slide 3: Approach to Update
Update of ANSI C63.14 must consider all Stakeholders:
  ANSI C63 Standards & US Industry
  US Military
    Referenced in MIL-STD-461E, MIL-STD-464A, MIL-HDBK-237, MIL-HDBK-240
  International Organizations
    IEC, NATO

## Slide 4: Proposed Update Approach
Update ANSI C63.14 by the following Steps:
  1. Review Recent & Old C63 Standards for new terms
  2. Review Selected Military References for new terms
    Review MIL-STD-461E, MIL-STD-464A, MIL-HDBK-237, -240
  3. Update Paragraph 2 References & review for new terms
    Capture any new IEC or NATO terms
  4. Propose Changes:
    Add Terms
    Delete Terms
      Found in IEEE Std 100 and
      Not EMC/ESD/EMP Specific or Related or used in ANSI C63 Documents
    Change Definitions of Terms
      Based upon Other ANSI C63 Standards & MIL-STDs
Get Consensus of C63 Main Group on Changes to Complete effort under this PINS

## Slide 5: Proposed Schedule
Steps | July 2004 | Oct 2004 | Jan 2005 | Apr 2005
1. Review recent ANSI C63 standards for new/changed terms |  |  |  | 
2. Review selected Military references for new/changed terms |  |  |  | 
3. Update Paragraph 2 References & review for new/changed terms |  |  |  | 
4. Propose Changes at ANSI C63 Meetings |  |  |  | 

## Slide 6: NEW TITLE?
Consider changing title
    From: American National Standard Dictionary for Technologies of Electromagnetic Compatibility (EMC), Electromagnetic Pulse (EMP), and Electrostatic Discharge (ESD)
    To: American National Standard Dictionary for Technologies of Electromagnetic Environmental Effects (E3)
Allows for Broader Scope of Terms for greater use by Military Standardization
  Consider current definition of E3 in C63.14
    Next page 

## Slide 7: E3 Definition in C63.14-1998
4.119 electromagnetic environment effects (E3). The impact of the electromagnetic environment upon the operational capability of electronic or electrical systems, equipments, or devices. It encompasses all electromagnetic disciplines, including the following:
  a) Electromagnetic compatibility;
  b) Electromagnetic interference;
  c) Electromagnetic vulnerability;
  d) Electromagnetic pulse;
  e) Electronic countermeasures;
  f) Hazards of electromagnetic radiation to ordnance and volatile materials;
  g) Natural phenomena effects of lightning and precipitation static (p-static). (NATO)
Changes to this Definition
proposed in a later slide

## Slide 8: SC/2 Activity Status

## Slide 9: ANSI C63 Documents
Following Documents Reviewed
  ANSI C63.2-1987
    American National Standard Guide for Instrumentation – Electromagnetic Noise and Field Strength, 10 kHz to 40 GHz - Specifications
  ANSI C63.5-1998
    American National Standard Guide for Electromagnetic Compatibility – Radiated Emission Measurements in Electromagnetic Interference (EMI) Control – Calibration of Antennas (9kHz to 40 GHz)
  ANSI C63.7-1992
    American National Standard Guide for Construction of Open-area Test Sites for Performing Radiated Emission Measurements
  ANSI C63.12-1999
    American National Standard recommended practice for electromagnetic compatibility limits
NOTE: ABOVE PUBLISHED DOCUMENTS LISTED IN IEEE XPLORE WEB SERVICE
Step 1.

## Slide 10: ANSI C63 Documents
Following Documents Reviewed
  ANSI C63.011-2000
    American national standard for limits and methods of measurement of radio disturbance characteristics of industrial, scientific, and medical (ISM) radio-frequency equipment
  ANSI C63.19-2001
    American National Standard for Methods of Measurement of Compatibility between Wireless Communication Devices and Hearing Aids
  ANSI C63.4-2003
    American national standard for methods of measurement of radionoise emissions from low-voltage electrical and electronic equipment in the range of 9 kHz to 40 GHz
NOTE: ABOVE PUBLISHED DOCUMENTS LISTED IN IEEE XPLORE WEB SERVICE
Step 1.

## Slide 11: ANSI C63 Documents
Following Documents to Review
  ANSI C63.16-2004?
    American National Standard for Electrostatic Discharge Test Methodologies and Criteria for Electronic Equipment
  ANSI C63.15-2004?
    Recommended Practice for Immunity Measurement of Electrical and Electronic Equipment
  ANSI C63.23-2004?
    Standard for Electromagnetic Compatibility – Computations and Treatment of Measurement Uncertainty
NOTE: ABOVE DRAFT DOCUMENTS STILL IN C63 SUBCOMMITTEES

## Slide 12: Review & Comparison of ANSI C63 Standards to C63.14
Step 1.

## Slide 13: Review & Comparison
ANSI C63.7-1992
    American National Standard Guide for Construction of Open-area Test Sites for Performing Radiated Emission Measurements
SAME | NEW
Just references C63.14-1992 | 

## Slide 14: Review & Comparison
  ANSI C63.5-1998
    American National Standard Guide for Electromagnetic Compatibility – Radiated Emission Measurements in Electromagnetic Interference (EMI) Control – Calibration of Antennas (9kHz to 40 GHz)
SAME | SAME
ambient level | radio noise
antenna factor (equivalent) | random noise
free-space antenna factor | site attenuation
ground plane | standard antenna calibration site
ideal site | 
normalized site attenuation | NEW
radiated emissions test site (reference test site) | No terms to add

## Slide 15: Review & Comparison
ANSI C63.12-1999
    American National Standard recommended practice for electromagnetic compatibility limits
SAME | NEW
electromagnetic disturbance | amplitude probability distribution (APD)
intersystem electromagnetic compatibility | atmospheric radio noise @
intrasystem electromagnetic compatibility | electromagnetic noise @
random noise | environmental radio noise @
 | noise amplitude distribution (NAD)
@ Recommended Additions to C63.14

## Slide 16: Review & Comparison
  ANSI C63.011-2000
    American national standard for limits and methods of measurement of radio disturbance characteristics of industrial, scientific, and medical (ISM) radio-frequency equipment
SAME | NEW
electromagnetic radiation* | ISM equipment; ISM appliance
Click* | boundary of the equipment under test
  *Note: definitions are similar to C63.14
  New terms will modify those terms in C63.14

## Slide 17: Review & Comparison
ANSI C63.19-2001
    American National Standard for Methods of Measurement of Compatibility between Wireless Communication Devices and Hearing Aids
SAME | NEW
emission bandwidth (B) | accessibility
transverse electromagnetic (TEM) cell* (better definition) | articulation weighting factor
 | audio coupling mode
 | audio frequency
 | audio band
 | audio band magnetic signal—desired (ABM1)
 | audio band magnetic signal—undesired (ABM2)
  *Note: definition is better than current one in C63.14

## Slide 18: Review & Comparison
ANSI C63.19-2001 (continued)
    American National Standard for Methods of Measurement of Compatibility between Wireless Communication Devices and Hearing Aids
SAME | NEW
 | audio band magnetic (ABM) articulation weighting factor (AWF)
 | Band
 | Compatibility
 | digital wireless telephone @
 | directional coupler @
 | far-field region (modify current def)
 | forward power @
 | hearing aid
@ Recommended Additions to C63.14

## Slide 19: Review & Comparison
ANSI C63.19-2001 (Continued)
SAME | NEW
 | input referenced interference level (IRIL)
 | intentional radiator @
 | measurement reference point:
 | near-field region
 | net power @
 | personal communications service device
 | reflected power @
 | sound pressure level (SPL)
 | tele-coil (T-coil)
 | wideband TEM (WB TEM) cell
 | wireless communications device (WD)

## Slide 20: Titles of C63 Standards Reviewed
ANSI C63.12-1999
    American National Standard recommended practice for electromagnetic compatibility limits
  ANSI C63.011-2000
    American national standard for limits and methods of measurement of radio disturbance characteristics of industrial, scientific, and medical (ISM) radio-frequency equipment
  ANSI C63.19-2001
    American National Standard for Methods of Measurement of Compatibility between Wireless Communication Devices and Hearing Aids
  ANSI C63.4-2003
    American national standard for methods of measurement of radionoise emissions from low-voltage electrical and electronic equipment in the range of 9 kHz to 40 GHz

## Slide 21: Non-C63 Documents
Following Documents Reviewed
  MIL-STD-461E, MIL-STD-464A
  MIL-HDBK-240, MIL-HDBK-237
  IEEE Std 100 (Reference Used Terms)
    For Duplicative Terms also in C63.14
  Results of review found new terms
    Discussed in next section
Step 2.

## Slide 22: New Terms to Add to C63.14

## Slide 23: New Terms from ANSI C63 Documents
Suggested Additions:
  atmospheric radio noise
  electromagnetic noise
  environmental radio noise
  digital wireless telephone
  directional coupler
  far-field region
  forward power
  intentional radiator
  net power
  reflected power
Results from Step 1.

## Slide 24: New Definitions (C63 docs)
From ANSI C63.12-1999:
  atmospheric radio noise
    Electromagnetic noise in the radio frequency range having its sources in natural atmospheric phenomena.
  electromagnetic noise
    A time-varying electromagnetic phenomenon apparently not conveying information and that may be superimposed on or combined with a wanted signal.
  environmental radio noise
    The total electromagnetic disturbance complex in which an equipment subsystem or system may be immersed, exclusive of its own electromagnetic contribution.
  directional coupler
    A transmission coupling device for separately (ideally) sampling (through a known coupling loss for measuring purposes) either the forward (incident) or the backward (reflected) wave in a transmission line.

## Slide 25: New Definitions (C63 docs)
From ANSI C63.19-2001:
  forward power
    That power supplied by the output of an amplifier (or generator) traveling towards a load. [SAE J551/1]
  intentional radiator
    A device that intentionally generates and emits radio frequency energy by radiation or induction. [FCC 15.3(o)]

## Slide 26: New Definitions (C63 docs)
From ANSI C63.19-2001:
  net power
    Forward power minus reflected power at the same location on a transmission line. [SAE J551/1]
  reflected power
    That power traveling towards the amplifier (or generator) reflected by a load caused by impedance mismatch between the transmission line and load. [SAE J551/1]

## Slide 27: New Terms from MIL-STDs
Suggested Additions:
  Electrically initiated device (EID) (MIL-STD-464A)
  Lightning direct effects (MIL-STD-464A)
  Lightning indirect effects (MIL-STD-464A)
  Multipaction (MIL-STD-464A)
  Non-developmental item (NDI) (MIL-STD-464A)
Results from Step 2.

## Slide 28: New Definitions from 464A
Electrically initiated device (EID) (MIL-STD-464A)
  An EID is a single unit, device, or subassembly that uses electrical energy to produce an explosive, pyrotechnic, thermal, or mechanical output. Examples include: electroexplosive devices (such as hot bridgewire, semiconductor bridge, carbon bridge, and conductive composition), exploding foil initiators, laser initiators, burn wires, and fusible links.
Lightning direct effects (MIL-STD-464A)
  Any physical damage to the system structure and electrical or electronic equipment due to the direct attachment of the lightning channel and current flow. These effects include puncture, tearing, bending, burning, vaporization, or blasting of hardware.
Lightning indirect effects (MIL-STD-464A)
  Electrical transients induced by lightning due to coupling of electromagnetic fields.

## Slide 29: New Definitions from 464A
Multipaction (MIL-STD-464A)
  Multipaction is a radio frequency (RF) resonance effect that occurs only in a high vacuum where RF field accelerates free electrons resulting in collisions with surfaces creating secondary electrons that are accelerated resulting in more electrons and ultimately a major discharge and possible equipment damage.
Non-developmental item (NDI) (MIL-STD-464A)
  Non-developmental item is a broad, generic term that covers material, both hardware and software, available from a wide variety of sources with little or no development effort required by the Government.

## Slide 30: New Definitions from 240, 237
MIL-HDBK-240 HERO Guide
  Terms added: Dudding, Electromagnetic Environment (EME), HERO, HERO Margins, Maximum Allowable Environment (MAE), Maximum No-Fire Current (MNFC), Maximum No-Fire Stimulus (MNFS), Reliability Consequence, Response Time (HERO), Safety Consequence (hard), Safety Consequence (soft)
MIL-HDBK-237
  Spectrum Management (SM)

## Slide 31: Terms to Delete from C63.14

## Slide 32: Proposed Term Deletions
Suggested Deletion (cited source):
  4.253 photon noise (C63.14-1998, ?)
Above term also found in IEEE Std 100-2000

## Slide 33: Improvement of Definitions of Terms in C63.14

## Slide 34: Proposed Term Changes
Suggested Definition Changes to:
  Electromagnetic environmental effects
    From MIL-STD-464A
  Transverse electromagnetic (TEM) cell
    From ANSI C63.19-2001

## Slide 35: Suggested Definition Change
Electromagnetic environmental effects
  MIL-STD-464A: The impact of the electromagnetic environment upon the operational capability of military forces, equipment, systems, and platforms. It encompasses all electromagnetic disciplines, including electromagnetic compatibility; electromagnetic interference; electromagnetic vulnerability; electromagnetic pulse; hazards of electromagnetic radiation to personnel, ordnance, and volatile materials; and natural phenomena effects of lightning and p-static.
  C63.14-1998: The impact of the electromagnetic environment upon the operational capability of electronic or electrical systems, equipments, or devices. It encompasses all electromagnetic disciplines, including the following:
  a) Electromagnetic compatibility;
  b) Electromagnetic interference;
  c) Electromagnetic vulnerability;
  d) Electromagnetic pulse;
  e) Electronic countermeasures;
  f) Hazards of electromagnetic radiation to personnel (HERP), ordnance (HERO) and fuel (volatile materials) (HERF);
  g) Natural phenomena effects of lightning, electrostatic discharge (ESD) and precipitation static (p-static). (NATO MIL-STD-464A)
Delete words in red, add words in green.
MODIFIES

## Slide 36: Suggested Definition Addition
NEW - C63.19-2001, paragraph 3.1.26:
  transverse electromagnetic (TEM) cell:
  (2) A measuring device that is designed to utilize the transverse electromagnetic (TEM) mode over the frequency range of interest. Common examples are the two port TEM cell (also known as the Crawford Cell) and the wideband TEM cell. (ANSI C63.19-2001)
Old - C63.14-1998: 4.365 transverse electromagnetic (TEM) cell:
  (1) An enclosed system, often a rectangular coaxial line, in which a wave is propagated in the transverse electromagnetic mode to produce a specified field level for testing purposes. [IEC 60050-161 (1990-09)]
ADD
Delete words in red, add words in green.

## Slide 37: Future Activity

## Slide 38: Future Effort
Review Draft ANSI C63 Documents
  ANSI C63.16-2004?
    American National Standard for Electrostatic Discharge Test Methodologies and Criteria for Electronic Equipment
  ANSI C63.15-2004?
    Recommended Practice for Immunity Measurement of Electrical and Electronic Equipment
  ANSI C63.23-2004?
    Standard for Electromagnetic Compatibility – Computations and Treatment of Measurement Uncertainty
Update Paragraph 2 References
  Review for new terms from National, Military, NATO and IEC documents