## Slide 1: FCC Update
Given by Martin Perrine
William Hurst
Chief, Technical Research Branch
Federal Communications Commission
Office of Engineering and Technology
Laboratory Division

## Slide 2: Digital Television
Public Notice
  OET Clarifies Emission Mask Measurements for DTV Transmitters
  DA 05-1321, May 10, 2005
NOI
  Technical Standards for Determining Eligibility For Satellite-Delivered Network Signals Pursuant To the Satellite Home Viewer Extension and Reauthorization Act
  ET Docket No. 05-182 (FCC 05-94)
Notes: Emission Mask Measurements
The out-of-channel emissions requirements for full service and low power DTV transmitters are specified for a measurement bandwidth of 500 kHz and are defined as attenuations relative to the total in-channel power. The rules also state that measurement bandwidths narrower than 500 kHz are permitted if appropriate correction factors are applied.
Direct measurement of such emissions with a 500 kHz resolution bandwidth (RBW) may not be possible because 500 kHz RBW may not be available on available measurement equipment. In addition, because resolution filters on spectrum analyzer do not have “brick wall” responses, leakage of the main DTV signal into the skirts of the resolution filter can corrupt out-of-channel emission measurements sufficiently to cause an apparent failure to satisfy the mask.
Two alternate methods have been described in the public notice.
Notice of Inquiry
Request comments as to whether existing statues and/or regulations concerning the digital television signal strength standard and testing procedures as used for identifying if household are unserved by local network TV signals for purpose of deferring eligibility to receive distant signals from satellite service need to be revised. The record obtained thouergh this inquiry will be used to prepare a report to Congress describing the results of this study and the Commission’s recommendations, if any, for changes that should be made to the applicable Federal status or regulations.

## Slide 3: Hearing Aid Compatibility
FCC Public Notice
  DA 05-1134
  April 25, 2005
OET Clarifies Use of Revised Wireless Phone Hearing Aid Compatibility Standard
Measurement Procedures and Rating Nomenclature
Notes: Applicants for certification to the HAC requirements may rely on either the 2001 or 2005 version of ANSI C63.19 and must identify which version they are using for compatibility testing and for rating wireless phones.
September 16, 2005 deadline for providing handsets models that comply with the radio frequency interference requirements of §20.19(b)
TCBs are allowed to certify these handsets.
Standard has updated the nomenclature for specify the radio frequency interference and inductive coupling of wireless phones to make it easier for consumers to understand.

## Slide 4: UPCS
Public Notice
  Unlicensed PCS Devices will no longer be subject to coordination requirements after April 4, 2005
  DA 05-1005
  April 4, 2005
Notes: This Public Notice is issued to clarify the equipment authorization requirements for Unlicensed Personal Communications Service (UPCS) devices that operate in the 1920-1930 MHz band pursuant to Subpart D of Part 15 of the Commission’s Rules. Specifically, we will no longer require, as part of our equipment authorization process, that UPCS equipment designed to operate under these rules incorporate certain coordination features and labeling features.
These relocation procedures are contained in Section 101.69 et seq. of the Commission’s Rules, and have guided the introduction of Emerging Technology licensees – including UPCS operations – into spectrum that the Commission previously reallocated from the Fixed Microwave Service. The sunset date represents a ten-year period after the date that voluntary relocation negotiations began for the first licensees in the 1850-1990 MHz band. Previously, on February 9, 2005, UTAM, Inc. (which is designated to coordinate and manage the transition in this band), submitted a letter to the Commission asking that we announce that the need for coordination of UPCS devices will no longer be required for those devices marketed after April 5.

## Slide 5: Garage Door Opener
Public Notice
  Consumers May Experience Interference To Their Garage Door Opener Controls Near Military Bases
  DA 05-424
  February 15, 2005
Notes: Consumers near certain military installations have recently experienced interference to their garage door opener controls that may reduce the operating distance or cause the device to stop operating. This public notice is issued to explain the cause of the interference and the steps being taken to alleviate this problem. The vast majority of consumers will not experience any interference to their garage door opener controls.
Garage door openers operate, legally under Part 15 of the Commissions rules, at very low power on an “unlicensed basis,” and have been permitted to operate on frequencies that have been reserved for the federal government since WWII for air/ground communications systems, but received limited use by the government for many years. As unlicensed devices, there is no right to protection from interference. However, because of this limited use, the risk of interference was similarly limited, so manufacturers of garage door openers chose these frequencies for their transmit and receive devices. In response to the increased needs of homeland security, the Department of Defense now must make more use of these frequencies to deploy new mobile radio systems on and around certain military bases.

## Slide 6: UNII
FCC Public Notice
  DA 05-175
  January 26, 2005
OET clarifies equipment authorization policy for Unlicensed National Information Infrastructure (U-NII) Devices operating in the 5 GHz band
Notes: In the 5 GHz U-NII Report and Order, ET Dkt No. 03-122, 18 FCC Rcd 24484 (2003), the Commission required, among other things, that U-NII devices operating in the 5.250-5.350 GHz band employ dynamic frequency selection (DFS) to ensure protection of Federal Government radar systems. Prior to initiating a transmission, a U-NII device’s DFS mechanism would monitor the available spectrum in which it could operate for a radar signal. If a signal were to be detected, the channel associated with the radar signal would either be vacated and/or flagged as unavailable for use by the U-NII device.
Applications for initial equipment certification filed after January 20, 2005 for U-NII equipment operating in the 5.250-5.350 GHz band must meet the rules adopted in the 5 GHz U-NII Report and Order. In addition, to prevent equipment without DFS capabilities from being imported and marketed indefinitely, equipment designed to operate in the 5.250-5.350 GHz band cannot be marketed or imported after January 20, 2006. See 47 C.F.R. § 15.37(l).
The FCC, National Telecommunications & Information Administration (NTIA), the Department of Defense (DOD) and the industry have been developing the testing methodologies for ensuring that DFS adequately protects Federal Government radar systems. As a result, measurement procedures for certifying U-NII devices containing DFS capabilities have not yet been finalized. All parties are currently working together to reach an agreement and expect that remaining issues will be resolved expeditiously.
In light of these circumstances and pursuant to Section 0.241(b) of the Commission’s Rules, OET will not apply the January 20, 2005 cut-off date for applications for certification of U-NII equipment operating without DFS or transmit power control (TPC) in the 5.250-5.350 GHz band for a period of sixty (60) days, effective immediately upon release of this Public Notice. The Commission will issue further guidance on this matter shortly.

## Slide 7: UWB
Petition for Waiver of the Part 15 UWB Regulations Filed by the Multi-band OFDM Alliance Special Interest Group
Notes: The Federal Communication Commission (FCC) adopted an Order in ET Docket No. 04-352 permitting radiated emissions from ultra-wideband (UWB) transmitters to be measured while the transmitter is in its normal operating mode. This waiver responds to the petition filed by the Multi-band OFDM Alliance Special Interest Group. The waiver provides greater flexibility and innovation in designing UWB devices.
The Commission previously established regulations permitting the marketing and operation of products incorporating UWB technology. Because UWB devices operate on the same frequency bands used by licensed stations, the Commission established a conservative procedure to measure the levels of radio frequency emissions generated by these devices. UWB transmitters that employ frequency hopping techniques must be measured with the hop stopped and the transmitter operating in a continuous mode; UWB transmitters that gate the emissions on and off must be measured with the emissions gated on. These procedures can result in measured emission levels that are greater than the UWB signal levels under actual operation.
In today’s Order, the Commission is providing a waiver of the existing measurement procedure, permitting emissions from UWB transmitters to be determined with the transmitter operating normally. The Commission concluded that this would not result in increased harmful interference to licensed radio operations. This waiver applies only to indoor or handheld UWB devices. Further, UWB devices utilizing this waiver may not operate within the 5030-5650 MHz band used for aircraft landing systems and for weather radars. A decision to permit this waiver to apply to UWB devices that operate within the 5030-5650 MHz band will be made upon the completion of the interference investigation being performed by the Institute for Telecommunication Sciences. The waiver is effective until the Commission finalizes a rule making proceeding dealing with these measurement issues.

## Slide 8: Future Items
Hearing Aid Compatibility (HAC)
802.11 measurement procedures
Dynamic Frequency Selection (DFS)
RF Exposure – above 3 GHz
Broadband over Powerline

## Slide 9: Discussion
TCB Council has been very active in providing educational opportunities for TCBs.
A need has been identified to provide educational opportunities on measurement methods and procedures for EMC test laboratories.
Suggestions on methods to provide information and education on new measurement methods to EMC Laboratories and Manufacturers.

## Slide 10: Thank You
Given by
Martin Perrine
William Hurst
Chief, Technical Research Branch
Federal Communications Commission
Office of Engineering and Technology
Laboratory Division
William.Hurst@fcc.gov