## Slide 1: Common Measurement Errors and Application Issues
ISED – C63 presentation – May 2026

## Slide 2: Purpose & Expectations
Purpose
Highlight common application, radio, and RF exposure errors identified during recent reviews
Promote consistent interpretation and application of current ISED requirements
Reduce application delays and passbacks through improved submission quality
ISED Expectations
Certification Bodies (CBs) are responsible for thorough technical review prior to submission
Only current, accepted standards, test methods, and FCC KDBs shall be used
Systemic issues must be identified and addressed through CB quality systems
Expected Outcomes
Fewer passbacks and faster REL listings
Improved consistency across applications
Greater confidence in compliance assessments
Take note of issues identified to improve the application review process

## Slide 3: Agenda
Important Notes on Applications
Radio Issues

## Slide 4: Important Notes on Applications

## Slide 5: Filing and Passback process
ISED performs reviews on technical briefs submitted for REL listing
ISED’s expectation when a file is passed back:
CB takes action on that particular file,
CB implements corrective measures (if required) to ensure that similar issues do not occur repeatedly
Passback trends need to be identified, and corrective measures implemented by CABs
ISED will take appropriate actions when systemic and/or critical problems are identified
ISED expects an email response prior to actioning a returned file
ISED considers passbacks as a complaint, this needs to be recorded as such in your quality system
Note: In major cases, ISED intends to copy the AB on the passback emails
ISED expects that a CB reviews any updates performed by a Test laboratory prior to re-submitting to ISED

## Slide 6: Normative Test methods
ANSI/USEMCSC C63.10 (methods of measurement for unlicensed wireless devices):
Since January 6, 2026:
  ANSI C63.10-2020+Cor. 1-2023+C63.10a-2024 + Errata to C63.10a-2024
ANSI C63.10-2013 is no longer a valid test method for licence-exempt devices, this includes using a KDB to reference this method.
ETSI EN 301 893 (methods for DFS compliance): v1.8.1 or v2.2.1 up to July 20, 2026
only v2.2.1 after July 20, 2026

## Slide 7: Passbacks – Report Consistency Issues
Some revised reports being received in response to a passback have significantly different results, including but not limited to:
  Output power changes
  Spurious emissions, harmonics no longer present
  SAR hotspot location changed
CB review should include comparison against the previous report version
Significant result changes should be clearly justified and reviewed by the CB prior to resubmission
Unexplained changes between report versions may be treated as potential measurement or process deficiencies

## Slide 8
Application documentation
All required documents were not completed appropriately
Consistency was not maintained throughout the documentation
Modular approval filing must contain an RSP-100 Annex D properly demonstrating how the device qualifies as a module
Documents were not uploaded
General Issues - Application
Any of the following errors will cause delays in the REL listing and lead to a passback to the Certification Body for amendments

## Slide 9
Application documentation
REL listing entries and documentation do not match
Data reuse applications must include the reference model test reports, especially when the reference model is not certified in Canada. Pre‑approval is required for data re-use applications.
Desired listing dates were not confirmed with a letter from the applicant
General Issues – Application Cont’d
Applications Note : ISED takes false declarations seriously, which may result in suspension from the REL and removal from the Canadian market

## Slide 10: General Issues – Report details
Report details
The reporting requirements in RSS-Gen are normative. All test reports must contain the details outlined in RSS-Gen Annex A
Details regarding the software used by the equipment under test, such as power level settings, software version used and operational configuration (such as SISO/MIMO or duty cycle)
Reports are often missing items such as, but not limited to:
Details of how worst-case conditions were determined
Block Diagrams

## Slide 11: General Issues – Report details cont’d
Report details
Reports are often missing items such as, but not limited to:
Correction factors – need to be explained and match block diagrams
Test equipment in the equipment list, specifically passive devices like attenuators, splitter/couplers, filters or cables, including calibration information
EUT identification, HVIN information
e.g. block diagram has an attenuator, but no corrections
CAB Identifier

## Slide 12: Radio Issues
Any of the following errors will cause delays in the REL listing and lead to a passback to the Certification Body for amendments

## Slide 13: Common Testing Errors
Spurious emissions methods of C63.10-2020 require spectral plots.
Tabular data is insufficient.
Noise floor
Measurement system sensitivity must comply with the noise floor requirements of C63.10-2020 above 1 GHz.
This includes Peak detector being used to demonstrate compliance with AVG detector limits.
Spectral Plots
External Controls
Demonstration of compliance with the external control requirements of RSS-119 is not always clear in the documentation. VFO mode – typically is considered external controls as it allows the user to select any frequency

## Slide 14: Common Testing Errors - cont’d
Unwanted emissions limits below 1 GHz apply to each operating band.
Testing once does not cover all bands of operation.
WPT Load
Cellphones used during RSS-216 testing must be capable of all operational modes of the WPT source; this may require modified cellphones.
Emissions below 1 GHz
Array Gain
MIMO gain must be calculated as per the normative measurement methods Array gain must be accounted for when required

## Slide 15: Common Testing Errors - cont’d
Detector type is determined by the mask (RSS-119 Mask B/D/E/F/Y require a Peak detector, not average) Span used to evaluate the emission mask must be sufficient to encompass the enter range specified within the mask
Industrial Zone Enhancers
Gain assessments must demonstrate measured gain must be ± 1 dB of the nominal
RSS-119 zone enhancers must comply with intermodulation and noise ERP limits, these are mandatory
Emission Masks
Reference Standards
Test methods must be those accepted by ISED, via either RSS-GEN or the KDB acceptance page. TIA-603 is not a listed reference standard

## Slide 16: FCC KDB usage for ISED Certification
FCC KDBs accepted by ISED
ISED maintains a list of accepted FCC KDBs which is published online:
http://www.ic.gc.ca/eic/site/ceb-bhst.nsf/eng/h_tt00094.html
CBs can follow guidelines within accepted KDBs and submit applications to SpectraWeb without prior consultation with ISED, unless the KDB requires consultation with the FCC
ISED expects the technical brief to highlight which accepted KDBs were used for product testing guidelines

## Slide 17: FCC KDB usage for ISED Certification (continued)
FCC KDBs not accepted by ISED
Many FCC KDBs are not on ISED’s list of accepted FCC KDBs;
CBs who have received FCC guidance via a KDB which is not on ISED’s list of accepted KDBs must contact ISED by email and seek acceptance of guidelines in this FCC KDB
ISED will not accept applications where KDB guidance was followed and the KDB was:
  Not on ISED’s list of accepted KDBs;
  Not accepted by ISED via a CB email request prior to submitting application;
  Not listed in the application technical brief as being a KDB accepted by ISED, including a copy of the specific KDB.

## Slide 18
Questions?