## Slide 1: FCC Updates
Alfonso G. Tarditi
Laboratory Division
Office of Engineering and Technology
Federal Communications Commission
Note: The views expressed in this presentation are those of the authors and may not necessarily represent the views of the Federal Communications Commission.

## Slide 2: Contents
Faster Path to Use of Standards for FCC Compliance
Good Topics for KDB-Endorsed Standards
The Antenna Boresight Issue in the C63.4 Annex
New KDB Pub. 231607 on Standards
Concluding Remarks

## Slide 3: Faster Path to Use of Standards for FCC Compliance (I)
Challenge: Bottleneck of Standard Adoptions in the FCC rules
KDB-Endorsed Technical Standards: a reference to Technical Standards is provided in the KDB Publication guidance (for compliance test procedures).
Incorporation-By-Reference process is slow, but technical standards referred through KDB guidance can gain priority in the acceptance process.
KDB Pubs.:
  do not require rulemaking action,
  are by design always compliant with the rules (or more conservative),
  are not binding [47 CFR 2.1093(d)(2)]
KDB Pubs. can be immediately updated when a new rulemaking is issued.
1Eyram Kunawotor, OET Lab., main author) ―

## Slide 4: Faster Path to Use of Standards for FCC Compliance (II)
The Advantage of KDB-Endorsed Technical Standards
KDB-Endorsed Standards will be considered as enabler/facilitators for reviewing equipment authorization applications (certifications).
Industry will benefit with reduced time-to-market and a more consistent and predictable authorization process.
KDB-endorsed Technical Standards will gain relevance in the international arena and get validated through widespread use in new certifications.
1Eyram Kunawotor, OET Lab., main author) ―

## Slide 5: Faster Path to Use of Standards for FCC Compliance (III)
Process Improvement
As happened in the past, and perhaps stating the obvious, prioritize development of Technical Standards by focusing on selected/critical compliance topics.
Look for feedback from test labs on common procedures required for FCC compliance but lacking sufficient specification.
Propose for needed updates that may reduce test time and equipment cost (without compromising result quality).

## Slide 6: Good Topics for KDB-Endorsed Standards (I)
Technologies in Evolution
U-NII 6 GHz: spectrum-sharing coexistence and incumbent concerns lead to high procedural complexity. This applies to standard power devices with AFC, low-power indoor and very-low-power devices, and test methods for coexistence and geolocation. Device-level test compliance procedures for dynamic and database-driven systems are key items.
Millimeter-wave and above-40 GHz measurements. Over-the-air methods, far-field distance, antenna arrays and beamforming, and test site validation above 18 GHz are still being worked out; C63.25.1 stops at 18 GHz.
Sub-THz emission measurements (at least up to 750GHz) in line with/expanding on KDB 800303 guidance.

## Slide 7: Good Topics for KDB-Endorsed Standards (II)
More Guidance Needed for the Labs
Multi-radio, MIMO and software-defined devices. Examples are simultaneous transmission, aggregate power and emissions with many antennas, and reconfigurable radios. Guidance on which configurations and software states must be tested.
Part 18 devices (including, but not limited to wireless power transfer):
  FCC compliance is about emission limits, not DUT power: a 1 MW well-shielded DUT may pass, while a 10 W poorly designed gadget may fail.
  Compliance is not based on what the device is used for, but on its emissions.
  High-power WPTs (for EVs, etc.) and other ISM devices may not need any special procedures as opposed to similar, but lower-power, designs.

## Slide 8: Good Topics for KDB-Endorsed Standards (III)
Procedural Items
Harmonization (e.g., CISPR and ETSI).
  Differences need to be justified on a technical basis.
  Industry will benefit from consistency among international standards to foster development of global products.
Total radiated power measurements in CATR chambers (e.g., quiet-zone requirements, chamber validation, positioner and sampling strategy).
Measurement uncertainty vs. compliance pass/fail.
  Compliance limits in FCC rules do not include uncertainties. Thus, uncertainties become a compliance margin (at best) or a market surveillance risk (more often).
  Consistent guidance on how to factor uncertainty in pass/fail decisions may steer product design towards lower risk without compromising performance.

## Slide 9: Good Topics for KDB-Endorsed Standards (IV)
Compliance Test Processes
Automation and remote testing. Standardized practices for automated test software, remote or unattended testing, and electronic reporting workflows.
Lab integrity and data authenticity:
  Increased FCC scrutiny and tightening oversight to prevent sloppy testing (at best) and unsecure product entry in the US market (more serious concern).
  Can a Technical Standard protect “good labs” by devising a process with intrinsically verifiable and traceable test data?
Data organization and accessibility: massive test reports obstruct the ability of TCBs and FCC reviews to verify compliance and slow down the certification process.

## Slide 10: The Antenna Boresight Issue in the C63.4 Annex
Preliminary Considerations
With a truly “omni” antenna, the result of a linear vs. boresight scan would be the same (this point basically summarizes the whole issue).
Even with an omni antenna, the received signal will still vary with height because of path length and ground reflection; that is fine because the change in slant distance and the ground reflections are part of the real effect that is meant to be measured through the height scan.
Boresight orientation keeps the antenna in the direction where the antenna factor is known (one could, in principle, choose another orientation, so long as any variation is accounted for).

## Slide 11: The Antenna Boresight Issue in the C63.4 Annex
Proposed Resolution on C63.4 Annex on Antenna Vertical Scan
When the receiving antenna is moved in height on a mast, the angle between the EUT and the antenna boresight changes, which introduces an error unless:
  the antenna is tilted to maintain boresight orientation, or
  there is a wide enough constant-directivity region, or
  a correction is applied.
If the antenna factor is constant (or within a stated tolerance) over the range of incidence angles encountered during the height scan, then the pattern-related error is negligible (or within the same tolerance) whatever the antenna's tilt.
A demonstrated estimate of this tolerance needs to be provided before a linear scan can be accepted via “padding” the results with the proven, sufficient margin.

## Slide 12: New KDB Pub. 231607 on Technical Standards (I)
Structure of the new publication (Draft for Comments until 10/27/2026)
INTRODUCTION
STANDARDS AND METHODS TYPICALLY USED FOR COMPLIANCE
  2.1 List Of Standards Accepted for Compliance Testing (Incorporated by Reference in FCC Rule Parts)
  2.2 List Of Other Standards Accepted for Compliance Testing (Not Incorporated by Reference in FCC Rule Parts)
LIST OF KDB PUBLICATIONS THAT REFER TO THE STANDARDS IN SECTION 2
  3.1 ANSI C63.4-2014
414788 D01 Radiated Test Site
460108 Antennas for radiated emission measurements below 30 MHz
….
3.2 ANSI C63.4a-2017
….

## Slide 13: New KDB Pub. 231607 on Standards (II)
Using the New KDB Pub. 231607 (Draft for Comments)
Lookup list of Technical Standards: for each of those, hyperlinks point to the KDB Publications refer to that Standard.
Look-up list of KDB Publications: for each of those, hyperlinks point to the Technical Standards referenced in that KDB Publication (reverse lookup of the previous item).

## Slide 14: New KDB Pub. 231607 on Standards (III)
Details
All KDB publications that refer to Technical Standards will be revised to remove the edition year; for example, instead of “C63.10-2013” there will be just “C63.10”.
In all KDB publications, any reference to a Technical Standard will point to the new KDB Pub. 231607 to identify the most up‑to‑date applicable version.
This will allow for efficient updates (i.e., by revising only KDB 231607) when a new edition of any Technical Standard is released.
Exceptions may be considered, and noted accordingly, if the guidance specifically requires content of an standard edition of a specific year.

## Slide 15: Conclusions
Coordination efforts with the FCC will facilitate the development of KDB publications that leverage Technical Standard content.
There are several topics highly relevant for FCC compliance that may benefit from Technical Standardization activities.
Maybe the solution of the boresight issue is in sight…
A new KDB Publication provides a synoptic view of Technical Standard references and use in the OET Lab published guidance for equipment authorization.